## Slide 1
Mitsubishi Electric Automation | Human Machine Interfaces 1
Selection Guide Edition 19 • Revised April 1, 2019
Category | Model Number | Screen Size | Resolution | Display Type | Frame Color | Power Supply | Stocked Item
GT2512 | GT2512-STBA | 12.1" | SVGA (800 x 600) | TFT Color | Black | 100-240VAC | S
 | GT2512-STBD |  |  |  |  | 24VDC | S
GT2510 | GT2510-VTBA | 10.4" | VGA (640 x 480) |  | Black | 100-240VAC | S
 | GT2510-VTBD |  |  |  |  | 24VDC | S
 | GT2510-VTWA |  |  |  | White | 100-240VAC | S
 | GT2510-VTWD |  |  |  |  | 24VDC | S
 | GT2510-WXTBD | 10.1" | WXGA (1280 x 800) |  | Black | 24VDC | S
 | GT2510-WXTSD |  |  |  | Silver | 24VDC | S
GT2508 | GT2508-VTBA | 8.4" | VGA (640 x 480) |  | Black | 100-240VAC | S
 | GT2508-VTBD |  |  |  |  | 24VDC | S
 | GT2508-VTWA |  |  |  | White | 100-240VAC | S
 | GT2508-VTWD |  |  |  |  | 24VDC | S
GT2507 | GT2507-WTBD | 7.0" | WVGA (800 x 480) |  | Black | 24VDC | S
 | GT2507-WTSD |  |  |  | Silver | 24VDC | S
 | GT2507T-WTSD (Rugged) |  |  |  | Silver | 24VDC | S
GT2505 | GT2505-VTBD | 5.7" | VGA (640 x 480) |  | Black | 24VDC | S
GT25 Series
GT25 Base Units
GT25 Power Supply Specifications
Model Number |  | GT2512-STBA GT2512F-STNA | GT2510-VTBA GT2510-VTWA GT2510F-VTNA | GT2508-VTBA GT2508-VTWA GT2508F-VTNA | GT2512-STBD GT2512F-STND | GT2510-VTBD GT2510-VTWD GT2510F-VTND | GT2508-VTBD GT2508-VTWD GT2508F-VTND | GT2505-VTBD
Input Power Supply Voltage |  | 100 to 240VAC (+10%, -15%) |  |  | 24VDC (+25%, -20%) |  |  | 24 VDC (+10%, -15%)
Input Power Supply Frequency |  | 50/60Hz ±5% |  |  | - |  |  | 
Power Consumption | Maximum Load | 35W or less | 34W or less | 31W or less | 37W or less | 33W or less | 31W or less | 8.4 W or less
 | Stand Alone | 14W | 12W | 11W | 13W | 10W | 8W | 4.3 W
 | Stand Alone with Backlight Off | 7W | 7W | 7W | 6W | 6W | 6W | 2.6 W
Inrush Current |  | 60A or less (2ms, ambient temperature 25°C, maximum load) |  |  | 5A or less (20ms, ambient temperature 25°C, maximum load) |  |  | 42 A or less (2 ms, ambient temperature: 25°C, under the maximum load)
Permissible Instantaneous Failure Time |  | Within 20ms (100VAC or more) |  |  | Within 10ms |  |  | 10 ms or less
Noise Resistance |  | Noise voltage 1500Vp-p, noise width 1μs by noise simulator with noise frequency 25 to 60Hz |  |  | Noise voltage 500Vp-p, noise width 1μs by noise simulator with noise frequency 25 to 60Hz |  |  | Noise voltage: 1000 Vp-p, noise width: 1 μs, measured by a noise simulator with noise frequency ranging from 30 Hz to 100 Hz
Withstand Voltage |  | 1500 VAC for 1 minute between power supply terminal and ground |  |  | 350 VAC for 1 minute between power supply terminal and ground |  |  | 500 VAC for 1 minute across power terminals and earth
Insulation Resistance |  | 10MΩ or higher with an insulation resistance tester (500 VDC between power supply terminal and ground) |  |  |  |  |  | 
Applicable Wire Size |  | 0.75 to 2 [mm²] |  |  |  |  |  | 
Clamp Terminal |  | Clamp terminals for M3 screw RAV1.25-3, V2-S3.3, V2-N3A, FV2-N3A |  |  |  |  |  | 
Tightening Torque (Terminal Block’s Terminal Screws) |  | 0.5 to 0.8 [N·m] |  |  |  |  |  | 
GT25 Open Frame Base Units
Category | Model Number | Screen Size | Resolution | Display Type | Frame Color | Power Supply | Stocked Item
GT25 Open Frame Model GOT (*1) | GT2512F-STNA | 12.1" | SVGA (800 x 600) | TFT color (65536 colors) | No frame | 100-240VAC | S
 | GT2512F-STND |  |  |  |  | 24VDC | S
 | GT2510F-VTNA | 10.4" | VGA (640 x 480) |  |  | 100-240VAC | S
 | GT2510F-VTND |  |  |  |  | 24VDC | S
 | GT2508F-VTNA | 8.4" | VGA (640 x 480) |  |  | 100-240VAC | S
 | GT2508F-VTND |  |  |  |  | 24VDC | S
Note 1: Always attach an environmental protection sheet dedicated to the open frame model (sold separately) to the display section. Or, attach a user-prepared environmental protection sheet. Not doing so may damage or soil the GOT or cause foreign matter to enter the GOT, resulting in a failure or malfunction

## Slide 2
2
HUMAN MACHINE INTERFACES
Selection Guide Edition 19 • Revised April 1, 2019
Model Number |  | GT2510-WXTBD • GT2510-WXTSD | GT2507-WTBD • GT2507-WTSD | GT2507T-WTSD
Input Power Supply Voltage |  | 24VDC (+25%, -20%) |  | 
Input Power Supply Frequency |  | - |  | 
Power Consumption | Maximum Load | 16 W or less | 16 W or less | 17 W or less
 | Stand Alone | 9 W or less | 9 W or less | 11 W
 | Stand Alone with Backlight Off | 5 W or less | 5 W or less | 7 W
Inrush Current |  | 59 A or less (2 ms, ambient temperature: 25°C, under the maximum load) |  | 
Permissible Instantaneous Failure Time |  | 5 ms or less |  | 
Noise Resistance |  | Noise voltage 500Vp-p, noise width 1μs by noise simulator with noise frequency 25 to 60Hz |  | 
Withstand Voltage |  | 350 VAC for 1 minute between power supply terminal and ground |  | 
Insulation Resistance |  | 10MΩ or higher with an insulation resistance tester (500 VDC between power supply terminal and ground) |  | 
Applicable Wire Size |  | 0.75 to 2 [mm²] |  | 
Clamp Terminal |  | Solderless terminal for M3 screw RAV1.25-3, V2-S3.3, V2-N3A, FV2-N3A |  | 
Tightening Torque (Terminal Block’s Terminal Screws) |  | 0.5 to 0.8 [N·m] |  | 
GT25 Power Supply Specifications (continued)
Screen Size | Model | A | B | Remarks
12.1" | GT2512 | 302 (11.89) | 228 (8.98) | Same dimensions as GT1685, GT1585, A985GOT
 | GT2512F | 214 (8.43) | 269 (10.59) | -
10.4" | GT2510 | 289 (11.38) | 200 (7.87) | Same dimensions as GT167_M, GT157_M, A97MGOT
 | GT2510F | 187 (7.36) | 234 (9.21) | -
10.1" | GT2510-WX | 243.5 (9.59) | 185.5 (7.30) | Panel thickness 1.6 (0.06) to 4 (0.16)
7" | GT2507-W | 180.5 (7.11) | 133.5 (5.26) | 
 | GT2507T-W | 197 (7.76) | 141 (5.55) | Panel thickness 1.6 (0.06) to 4 (0.16)
8.4" | GT2508 | 227 (8.94) | 176 (6.93) | Same dimensions as GT1665, GT1565
 | GT2508F | 158 (6.22) | 194 (7.64) | -
5.7" | GT2505 | 156 (6.02) | 121 (4.76) | Same dimensions as GT1455, GT1450
B +2 (0.08)
0 (0)
Panel opening
A +2 (0.08)
0 (0)
(unit: mm)
GT25 Panel Cut Dimensions

## Slide 3
Mitsubishi Electric Automation | Human Machine Interfaces 3
Selection Guide Edition 19 • Revised April 1, 2019
GT25 Performance Specifications
Model Number |  | GT2512-STBA GT2512-STBD | GT2512F-STNA GT2512F-STND | GT2510-VTBA GT2510-VTBD | GT2510-VTWA GT2510-VTWD | GT2510F-VTNA GT2510F-VTND | GT2510-WXTBD GT2510-WXTSD
Display Section (*1, *2) | Type | TFT color LCD |  |  |  |  | 
 | Screen Size | 12.1" |  | 10.4" |  |  | 10.1" Wide
 | Resolution (Dots) | 800 x 600 dots SVGA |  | 640 x 480 VGA |  |  | WXGA: 1280 × 800 dots
 | Display Size (W x H) mm | 246 x 184.5 |  | 211.2 x 158.4 |  |  | 216.96 x 135.6
 | Number of Characters | 16-dot standard font: 50 chars x 37 lines (2-byte) 12-dot standard font: 66 chars. x 50 lines (2-byte) |  | 16-dot standard font: 40 chars. × 30 lines (2-byte) 12-dot standard font: 53 chars. × 40 lines (2-byte) |  |  | 16-dot standard font: 80 characters × 50 lines (two-byte) 12-dot standard font: 106 characters × 66 lines (two-byte)
 | Display Colors | 65536 colors |  |  |  |  | 
 | Intensity Adjustment | 32-level adjustment |  |  |  |  | 
Backlight | Type | LED (not replaceable) |  |  |  |  | 
 | Life (*4) | Approx. 60000 hours or more (Time for display intensity reaches 50% at ambient temperature of 25°C) |  |  |  |  | Approx. 50000 h (operating ambient temperature: 25 °C, display intensity: 50%)
Touch Panel (*3) | Type | Analog resistive film |  |  |  |  | 
 | Key Size (Dots) | Minimum 2 x 2 dots (per key) (*8) |  |  |  |  | 
 | Simultaneous Press | Not available (*5) (only 1 point can be pressed) |  |  |  |  | 
 | Life | 1 million times or more (operating force 0.98N or less) |  |  |  |  | 
Panel Color |  | Black | - | Black | White | - | GT2510-WXTBD: Black GT2510-WXTSD: Silver
Memory | User Memory Capacity | Memory for storage (ROM): 32MB, Memory for operation (RAM): 80MB |  |  |  |  | Memory for storage (ROM): 32MB, Memory for operation (RAM): 128MB
 | Life (No. of Writings) | 100,000 times |  |  |  |  | 
Internal Clock Accuracy |  | ±90 sec/month (ambient temperature 25°C) |  |  |  |  | 
Battery | Type | GT11-50BAT lithium battery |  |  |  |  | 
 | Life | Approx. 5 years (ambient temperature 25°C) |  |  |  |  | 
Built-in Interface | RS-232 | 1ch Transmission speed: 115200/57600/38400/19200/9600/4800bps Connector shape: D-sub 9-pin (male) |  |  |  |  | 
 | RS-422/485 | 1ch Transmission speed: 115200/57600/38400/19200/9600/4800bps Connector shape: D-sub 9-pin (female) |  |  |  |  | 
 | Ethernet | 1ch Data transfer method: 10BASE-T/100BASE-TX Connector shape: RJ-45 (modular jack) |  |  |  |  | 2ch
 | USB (Host) | 2ch (front/rear face) | 1ch (rear face) | 2ch (front/rear face) | 1ch (rear face) |  | 
 |  | Maximum transfer speed: High-Speed 480Mbps Connector shape: USB-A |  |  |  |  | 
 | USB (Device) | 1ch (front face) | 1ch (rear face) | 1ch (front face) | 1 channel (rear face) |  | 1 ch (front face)
 |  | Maximum transfer rate: High-Speed 480 Mbps Connector shape: USB Mini-B |  |  |  |  | 
 | SD Memory Card | 1ch SDHC compliant (maximum 32GB) |  |  |  |  | 
 | Extension Interface | For communication unit/option unit mounting |  |  |  |  | -
 | Side Interface | For installing a wireless LAN communication unit |  |  |  |  | 
 | Sound Output Interface | - |  |  |  |  | 1 channel, WAV format (16 bits, 8 kHz/16 kHz, monoral) applicable plug: 3.5 stereo mini-plug (3-prong)
Buzzer Output |  | Single tone (tone, tone length adjustable) |  |  |  |  | 
Power LED |  | Emission color: 2 colors (blue, orange) |  |  |  |  | 
Protective Construction |  | Front: IP67F (*6, *9) Inside control panel: IP2X | Front: IP67F (*7, *9) Inside control panel: IP2X | Front: IP67F (*6, *9) Inside control panel: IP2X |  | Front: IP67F (*7, *9) Inside control panel: IP2X | Front: IP67F (*6*9) In control panel: IP2X
External Dimensions (W x H x D) mm |  | 316 x 246 x 52 | 311 x 237 x 54 | 303 x 218 x 52 |  | 298 x 209 x 54 | 252 x 194 x 48
Panel Cutout (W x H) mm |  | 302 x 228 | 269 x 214 | 289 x 200 |  | 234 x 187 | 243.5 x 185.5
Weight (Excluding Mounting Brackets) kg |  | 2.4 |  | 2.1 |  |  | 1.2
Applicable Software Package |  | GT Works3 Version1.122C or later | GT Works3 Version1.150G or later | GT Works3 Version1.112S or later |  | GT Works3 Version1.150G or later | GT Works3 Version 1.175H or later
Notes:
As a characteristic of liquid crystal display panels, bright dots (always lit) and dark dots (never lit) may appear on the panel. Since liquid crystal display panels comprise a great number of display elements, the appearance of bright and dark dots cannot be reduced to zero. Individual differences in liquid crystal display panels may cause differences in color, uneven brightness and flickering. Note that these phenomena are characteristics of liquid crystal display panels and it does not mean the products are defective or damaged.
Flickering may occur due to vibration, shock, or the display colors.
When a stylus is used, the touch panel has a life of 100 thousand touches. The stylus must satisfy the following specifications: • Material: polyacetal resin • Tip radius: 0.8 mm or more
To prevent the display section from burning in and lengthen the backlight life, enable the screen save function and turn off the backlight.
If you touch two points or more simultaneously on the touch panel, a touch switch near the touched points may operate unexpectedly. Do not touch two points or more simultaneously on the touch panel.
To conform to IP67F, close the USB environmental protection cover by pushing the [PUSH] mark firmly. (To conform to IP2X, open the USB environmental protection cover.) Note that the structure does not guarantee protection in all users’ environments. The GOT may not be used in certain environments where it is subjected to splashing oil or chemicals for a long period of time or soaked in oil mist.
To conform to IP67F attach the environmental protection sheet. Note that the structure does not guarantee protection in all users’ environments. The GOT may not be used in certain environments where it is subjected to splashing oil or chemicals for a long period of time or soaked in oil mist.
The minimum size of a key that can be arranged. To ensure safe use of the product, the following settings are recommended: • Key size: 16 x 16 dots or larger • Distance between keys: 16 dots or more
The suffix “F” of IP67F is a symbol that indicates protection rate against oil. It is described in the Appendix of Japanese Industrial Standard JIS C 0920.

## Slide 4
4
HUMAN MACHINE INTERFACES
Selection Guide Edition 19 • Revised April 1, 2019
Model Number |  | GT2508-VTBA GT2508-VTBD | GT2508-VTWA GT2508-VTWD | GT2508F-VTNA GT2508F-VTND | GT2507-WTBD GT2507-WTSD | GT2507T-WTSD | GT2505-VTBD
Display Section (*1, *2) | Type | TFT color LCD |  |  |  |  | 
 | Screen Size | 8.4" |  |  | 7" Wide |  | 5.7"
 | Resolution (Dots) | 640 x 480 VGA |  |  | WVGA:800 x 480 dots |  | 640 x 480 VGA
 | Display Size (W x H) mm | 170.9 x 128.2 |  |  | 152.40 x 91.44 |  | 115.2 x 86.4
 | Number of Characters | 16-dot standard font: 40 chars. × 30 lines (2-byte); 12-dot standard font: 53 chars. × 40 lines (2-byte) |  |  | 16-dot standard font: 50 characters × 30 rows (Two-byte characters) 12-dot standard font: 66 characters × 40 rows (Two-byte characters) |  | 16-dot standard font: 40 chars. × 30 lines (2-byte); 12-dot standard font: 53 chars. × 40 lines (2-byte)
 | Display Colors | 65536 colors |  |  |  |  | 
 | Intensity Adjustment | 32-level adjustment |  |  |  |  | 
Backlight | Type | LED (not replaceable) |  |  |  |  | 
 | Life (*4) | Approx. 60000 hours or more (Time for display intensity reaches 50% at ambient temperature of 25°C) |  |  | Approx. 50000 h (operating ambient temperature: 25°C, display intensity: 50%) |  | Approx. 60000 hours or more (Time for display intensity reaches 50% at ambient temperature of 25°C)
Touch Panel (*3) | Type | Analog resistive film |  |  |  |  | 
 | Key Size (Dots) | Minimum 2 x 2 dots (per key) (*8) |  |  |  |  | 
 | Simultaneous Press | Not available (*5) (only 1 point can be pressed) |  |  |  |  | 
 | Life | 1 million times or more (operating force 0.98N or less) |  |  |  |  | 
Panel Color |  | Black | White | - | GT2507-WTBD: Black GT2507-WTSD: Silver | Silver | Black
Memory | User Memory Capacity ROM (Storage) RAM (Operation) | ROM: 32MB; RAM: 80MB |  |  | ROM: 32MB; RAM: 128MB |  | ROM: 32MB; RAM: 80MB
 | Life (No. of Writings) | 100,000 times |  |  |  |  | 
Internal Clock Accuracy |  | ±90 sec/month (ambient temperature 25°C) |  |  |  |  | 
Battery | Type | GT11-50BAT lithium battery |  |  |  |  | 
 | Life | Approx. 5 years (ambient temperature 25°C) |  |  |  |  | 
Built-in Interface | RS-232 | 1ch Transmission speed: 115200/57600/38400/19200/9600/4800bps Connector shape: D-sub 9-pin (male) |  |  |  |  | 
 | RS-422/485 | 1ch Transmission speed: 115200/57600/38400/19200/9600/4800bps Connector shape: D-sub 9-pin (female) |  |  |  |  | 
 | Ethernet | 1ch |  |  | 2ch |  | 1ch
 | USB (Host) | 2ch (front/rear face) | 1ch (rear face) |  |  |  | 
 |  | Maximum transfer speed: High-Speed 480Mbps Connector shape: USB-A |  |  |  |  | 
 | USB (Device) | 1ch (front face) | 1ch (rear face) |  | 1ch (front face) | 1ch (rear face) | 1ch (front face)
 |  | Maximum transfer rate: High-Speed 480 Mbps Connector shape: USB Mini-B |  |  |  |  | 
 | SD Memory Card | 1ch SDHC compliant (maximum 32GB) |  |  |  |  | 
 | Extension Interface | For communication unit/option unit mounting |  |  | - | - | -
 | Side Interface | For installing a wireless LAN communication unit |  |  |  |  | -
 | Sound Output Interface | - |  |  | 1 channel, WAV format (16 bits, 8 kHz/16 kHz, monoral) applicable plug: ø3.5 stereo miniplug (3-prong) |  | -
Buzzer Output |  | Single tone (tone, tone length adjustable) |  |  |  |  | 
Power LED |  | Emission color: 2 colors (blue, orange) |  |  |  |  | 
Protective Construction |  | Front: IP67F (*6, *9) Inside control panel: IP2X |  | Front: IP67F (*7, *9) Inside control panel: IP2X | Front: IP67F (*6*9) In control panel: IP2X | Front: IP66F / IP67F (*9) In control panel: IP2X | Front: IP67F (*7, *9) Inside control panel: IP2X
External Dimensions (W x H x D) mm |  | 241 x 194 x 52 |  | 236 x 185 x 54 | 189 x 142 x 48 | 214 x 158 x 55 | 164 x 139 x 53.5
Panel Cutout (W x H) mm |  | 227 x 176 |  | 194 x 158 | 180.5 x 133.5 | 197 x 141 | 153 x 121
Weight (Excluding Mounting Brackets) kg |  | 1.5 |  |  | 0.75 | 1.2 | 0.6
Applicable Software Package |  | GT Works3 Version1.112S or later |  | GT Works3 Version1.150G or later | GT Works3 Version 1.175H or later |  | GT Works3 Version1.180N or later
GT25 Performance Specifications (continued)
Notes:
As a characteristic of liquid crystal display panels, bright dots (always lit) and dark dots (never lit) may appear on the panel. Since liquid crystal display panels comprise a great number of display elements, the appearance of bright and dark dots cannot be reduced to zero. Individual differences in liquid crystal display panels may cause differences in color, uneven brightness and flickering. Note that these phenomena are characteristics of liquid crystal display panels and it does not mean the products are defective or damaged.
Flickering may occur due to vibration, shock, or the display colors.
When a stylus is used, the touch panel has a life of 100 thousand touches. The stylus must satisfy the following specifications: • Material: polyacetal resin • Tip radius: 0.8 mm or more
To prevent the display section from burning in and lengthen the backlight life, enable the screen save function and turn off the backlight.
If you touch two points or more simultaneously on the touch panel, a touch switch near the touched points may operate unexpectedly. Do not touch two points or more simultaneously on the touch panel.
To conform to IP67F, close the USB environmental protection cover by pushing the [PUSH] mark firmly. (To conform to IP2X, open the USB environmental protection cover.) Note that the structure does not guarantee protection in all users’ environments. The GOT may not be used in certain environments where it is subjected to splashing oil or chemicals for a long period of time or soaked in oil mist.
To conform to IP67F attach the environmental protection sheet. Note that the structure does not guarantee protection in all users’ environments. The GOT may not be used in certain environments where it is subjected to splashing oil or chemicals for a long period of time or soaked in oil mist.
The minimum size of a key that can be arranged. To ensure safe use of the product, the following settings are recommended: • Key size: 16 x 16 dots or larger • Distance between keys: 16 dots or more
The suffix “F” of IP67F is a symbol that indicates protection rate against oil. It is described in the Appendix of Japanese Industrial Standard JIS C 0920.